## Slide 1
1
2
3
4

## Slide 2: Topic: J277.1.3.1 Title: Layers Date: 08/01/2026
Put today’s title and date.
Underline both

## Slide 3: Knowledge Objectives
The concept of layers | Required How layers are used in protocols, and the benefits of using layers; for a teaching example, please refer to the 4-layer TCP/IP model

## Slide 4: Keyword
Keyword: Layer
Description: In networking, a layer is a level or stage in a network model where a specific job or function is carried out to help data move from one device to another. Each layer has a defined role and works with the layers above and below it.
Synonyms: Level, stage, tier
GCSE tip: Network models (such as the OSI model) use layers to simplify networking by breaking complex processes into manageable parts.

## Slide 5: Sub-title: Layers
Write the sub-title and underline
Write the following:
  Layers: In order to simplify design, network protocols and devices operate at a specific level and only interact with the level above them and the level below them. The lower the level the simpler the communications taking place.

## Slide 6: Sub-title: OSI Model
The OSI model specifies 7 layers
  Application: End user layer (HTTP, FTP, IRC, SSH, DNS)
  Presentation: Syntax layer (The encoding/format of data: SSL, SSH, IMAP, FTP, JPEG, MPEG)
  Session: Synch & send to port (Ports, Sockets)
  Transport: End-to-end communications (TCP, UDP)
  Network: Packets (IP, ICMP)
  Data link: Frames (Ethernet, PPP, Switch, Bridge)
  Physical: Physical infrastructure (Coax, fibre-optic, wireless, hubs, repeaters)

## Slide 7: Sub-title: TCP/IP Model
Write the sub-title and underline
Write the following:
  TCP/IP model simplifies the OSI model and operates over 4 layers
    Application layer - (Provides services directly to users and applications)
      HTTP / HTTPS – used for accessing websites
      FTP – used to transfer files
      SMTP – used to send emails
      POP3 / IMAP – used to receive emails
      DNS – converts domain names into IP addresses
    Transport layer - (Controls how data is sent and received)
      TCP (Transmission Control Protocol)Reliable, checks for errors, guarantees delivery
      UDP (User Datagram Protocol)Faster but less reliable, no error checking
    Internet / Network layer - (Handles addressing and routing)
      IP (IPv4 / IPv6) – provides addressing and routing
      ICMP – used for error messages and diagnostics (e.g. ping)
    Network Access / Data Link layer(Handles physical transmission of data)
      Ethernet – wired network communication
      Wi-Fi (IEEE 802.11) – wireless network communication
      ARP – matches IP addresses to MAC addresses

## Slide 8: TCP/IP Stack
Place each of these protocols at the correct TCP/IP model layer
  DNS – converts domain names into IP addresses
  ICMP – used for error messages and diagnostics (e.g. ping)
  Ethernet – wired network communication
  UDP (User Datagram Protocol)Faster but less reliable, no error checking
  TCP (Transmission Control Protocol)Reliable, checks for errors, guarantees delivery
  Wi-Fi (IEEE 802.11) – wireless network communication
  ARP – matches IP addresses to MAC addresses
  FTP – used to transfer files
  SMTP – used to send emails
  HTTP / HTTPS – used for accessing websites
  IP (IPv4 / IPv6) – provides addressing and routing
  POP3 / IMAP – used to receive emails

## Slide 9: Exam Style Questions
Question 1 (2 marks)
  State what is meant by a layer in a network model.
Question 2 (3 marks)
  Name the four layers of the TCP/IP model and briefly describe the role of one of them.
Question 3 (3 marks)
  Explain how protocols use layers in the TCP/IP model to send data from one device to another.
Question 4 (4 marks)
Describe two benefits of using layers in network protocols.
Question 5 (4 marks)
  Explain why a problem at one layer of the TCP/IP model does not necessarily affect the other layers.
Question 6 (6 marks)
  A student says, “Using layers in network protocols makes networking more complicated.” Evaluate this statement, referring to the TCP/IP model in your answer.