## Slide 1
1
2
What is an IP address?
What is the format of an IP address?
3
What is a MAC address?
4
What is the format of a MAC address?

## Slide 2: Topic: J277.1.3.2 Title: Addressing Date: 21/04/2026
Put today’s title and date.
Underline both

## Slide 3: Knowledge Objectives
IP addressing and MAC addressing | Required IP addressing and the format of an IP address (IPv4 and IPv6) A MAC address is assigned to devices; its use within a network

## Slide 4: Sub-title: IP Addresses
IP addresses: are used to uniquely identify a device on an IP based network. With the increase in devices around the world connecting to the internet, IPv4 was replaced with IPv6.
  IPV4: addressing is a 32-bit address made up of 4 groups of 8-bit numbers. Each group has a range of 0-255 (256 different possibilities). The maximum number of unique addresses for the whole IP address is 2^32 (4,294,967,296).
  IPV6: addressing is a 128-bit address made up of 8 groups of 4 hexadecimal numbers. Each group has a range of 0000-FFFF (65,536 different possibilities). The maximum number of unique addresses for the whole IP address is 2^128 (340,282,366,920,938,000,000,000,000,000,000,000,000).

## Slide 5: Sub-title: MAC Addresses
MAC addresses: also known as Medium Access Control or hardware address is a 48-bit address made up of 12 Hexadecimal characters. The hardware address uniquely identifies a piece of hardware on the network.
The maximum number of possible unique addresses is 2^48 (281,474,976,710,656)

## Slide 6: Exploring
What is an IP address
What was IPv4 replaced with?
Why was IPv4 replaced?
What is the format of an IPv4 address?
What is the format of an IPv6 address?
What is a MAC address?
What is the format of a MAC address?

## Slide 7: Exploring
What is an IP address?
  A unique address assigned to a specific device on a LAN or WAN.
What was IPv4 replaced with?
  IPv6.
Why was IPv4 replaced?
  Not enough unique addresses for all internet devices.
What is the format of an IPv4 address?
  4 groups of numbers between 0 & 255 separated by dots. E.g. 192.168.1.8
What is the format of an IPv6 address?
  8 groups of 4-digit hexadecimal between 0000 and FFFF separated by colons. E.g. FFFF:FFFF:FFFF:FFFF:FFFF:FFFF:FFFF:FFFF
What is a MAC address?
  A unique address assigned to a specific piece of hardware used on a LAN.
What is the format of a MAC address?
  6 groups of 2-digit hexadecimal between 00 and FF. E.g. FF:FF:FF:FF:FF:FF

## Slide 8
WAN
LAN
80.15.26.73
Router
B8:27:EB:45:12:34
192.168.1.1
Computer
00:1A:2B:3C:4D:5E
192.168.1.2
Computer
A4:5E:60:7F:12:9B
192.168.1.3
Computer
F0:9F:C2:88:77:66
192.168.1.4
Printer
3C:52:82:AB:CD:EF
192.168.1.5
80.15.26.1
Router
D4:6A:6A:9C:8B:01
80.15.24.1
Router
D4:6A:6A:9C:8B:01
80.15.25.1
Router
9A:BC:DE:F1:23:45
WAN IP Address
Device
MAC Address
LAN IP Address

## Slide 9: Do routers have MAC addresses?
Yes — routers do have MAC addresses.
Why routers need MAC addresses
A router operates at both:
  Layer 3 (Network layer) → uses IP addresses to route traffic between networks
  Layer 2 (Data link layer) → uses MAC addresses to send data on a local network
How it works in practice
Every network interface on a router (e.g. Ethernet ports, Wi-Fi adapter) has its own MAC address
When devices on your local network (like a laptop) send data:
  They use the router’s MAC address as the destination (for the next hop)
  The router then forwards the packet using IP routing
Key points
A router doesn’t have just one MAC — it usually has multiple MAC addresses (one per interface)
Your device learns the router’s MAC address using ARP (Address Resolution Protocol)
On a home network, this is often the MAC address of the default gateway

## Slide 10: Example IP Routing table
Destination IP Subnet Mask Next Hop Interface MAC Address
-----------------------------------------------------------------------------------------------------------------------------------
192.168.1.0 255.255.255.0 0.0.0.0 eth0 00:1A:2B:3C:4D:5E
192.168.1.10 255.255.255.255 0.0.0.0 eth0 A4:5E:60:7F:12:9B
192.168.1.20 255.255.255.255 0.0.0.0 eth0 F0:9F:C2:88:77:66
192.168.1.30 255.255.255.255 0.0.0.0 eth0 3C:52:82:AB:CD:EF
192.168.1.40 255.255.255.255 0.0.0.0 eth0 B8:27:EB:45:12:34
192.168.1.50 255.255.255.255 0.0.0.0 eth0 D4:6A:6A:9C:8B:01
192.168.1.60 255.255.255.255 0.0.0.0 eth0 9A:BC:DE:F1:23:45
192.168.1.70 255.255.255.255 0.0.0.0 eth0 02:7F:A0:4C:9D:E8
0.0.0.0 0.0.0.0 192.168.1.1 eth1 (ISP Router MAC)

## Slide 11: Suitability of IPv4
When would IPv4 be better than using IPv6?
Using IPv4 would be better when connecting to older networks or legacy devices that do not support IPv6.
Why IPv4 is better in this case:
  IPv4 has wider compatibility with older hardware, software, and operating systems.
  Many existing networks and services are still configured primarily for IPv4.It can be simpler to set up and manage on small or older networks.
GCSE-style summary:
  IPv4 is better when compatibility with existing systems is more important than the need for a large number of IP addresses.

## Slide 12: Suitability of IPv6
When would IPv6 be better than using IPv4?
Using IPv6 would be better when setting up a large or modern network with many devices, such as a smart home, school, or business network.
Why IPv6 is better in this case:
  IPv6 provides a much larger number of IP addresses, allowing every device to have a unique address.
  It reduces or removes the need for NAT (Network Address Translation).
  It is designed for modern networks and the growing number of internet-connected devices (IoT).
  Supports more efficient routing and built-in features such as improved security support.
GCSE-style summary:
  IPv6 is better when a network needs many unique IP addresses and is being designed for future growth.

## Slide 13: Exam Style Questions
Question 1 (2 marks)
  State what an IP address is used for on a network.
Question 2 (3 marks)
  Describe the format of an IPv4 address.
Question 3 (3 marks)
  Explain one reason why IPv6 was introduced.
Question 4 (4 marks)
  Compare IPv4 and IPv6 in terms of:
    number of available addresses
    address format
Question 5 (2 marks)
  State two characteristics of a MAC address.
Question 6 (6 marks)
  A device is connected to a local network and the internet.
  Explain the roles of the MAC address and the IP address in allowing data to reach the correct device.